700/800 Systems

Frequency Selection Rules

- Frequency Spacing……………..…	Separate frequencies by least 300 kHz (400kHz preferred)

- IM Products………….……………	2 transmitter 3rd orders by at least 100kHz (200kHz preferred)

3 transmitter 3rd orders by at least 50kHz (100kHz preferred)

2 transmitter 5th orders by at least 50kHz (100kHz preferred)

- Transmitter Sidebands……...……	Avoid base and beltpack carrier sidebands: +/-200kHz, +/-400 and +/-600. Keep at least 50kHz away from these frequencies.

- Bandwidths………………….…….	Transmitter bandwidth = 100kHz

Receiver bandpass = 230kHz

- Base RX 4MHz Image Harmonics.	C6 frequencies to avoid are 704.4, 708.4, 712.4, 716.4.

A2 frequencies to avoid are 632.4, 636.4, 640.4, 644.4.

Avoid the frequencies, by at least 50kHz

- Base LO1 Xtal harmonics……...…	Avoid C6 Xtal harmonics; 524.667, 655.833, 787.000 by  at least 50kHz .

Avoid A2 Xtal harmonics; 476.667, 595.833, 715.000 by at least 50kHz.

# TR-700/800 Oscillators/IFs – Dual Conversion Superheterodyne, Synthesized, FM

LO1…………...……….…	Synthesized (If set on correct frequency then, LO1 = RFIN – 65.7)

LO2………………………	55MHz, Xtal, Fixed

Master Oscillator….…..…	4MHz, Xtal, trimmer adjust

IF1……………….……….	65.7MHz

IF2…………………….….	10.7MHz

Transmitter……………….Synthesized, FM

# BTR-700/800 Oscillators/IFs   - Dual Conversion Superheterodyne, Synthesized, FM

LO1………………………	X MHz, x6 Xtal Osc., Fixed

1 Band……….…	X = 697MHZ

2 Band……….…	X = 715MHz

3 Band……….…	X = 733MHZ

4 Band……….…	X = 751MHZ

5 Band……….…	X = 769MHz

6 Band……….…	X = 787MHZ

7 Band……….…	X = 805MHZ

Examples: A C6 system’s LO1 is set to the Band 6 (787MHz) frequency.  An A2 system’s LO1 is set to the Band 2 (715MHz) frequency.

LO2……………...…….…	Synthesized, 75.8 to 93.6MHz.  (If set on correct frequency then, LO2 = LO1 - RFIN + 10.7)

Master Oscillator...………	4MHz, Xtal, trimmer adjust

IF1……………….……….	65 – 83MHz

IF2…………….………….	10.7MHz

Transmitter(s)……………	Synthesized, FM