The 500DA-HD Reclocking Distribution Amplifier provides reliable distribution of your HD and SD SDI video signal at rates of 1.5Gb/s and 143Mb/s to 540Mb/s. The DA features an auto-equalized input with eight serial outputs.

The 500DA-HD has been designed for use as a SMPTE 292M (1.5Gb/s), DVB-ASI, SMPTE 259M, or SMPTE 310M distribution product.

The 500DA-HD DAs are housed in the 3RU 500FR frame that will hold up to 16 modules.

Features & Benefits:

• Normal mode for SMPTE 259M (143-540Mb/s) or SMPTE 292M (1.5Gb/s)

signals - autodetects correct bitrate

• Jumper selectable mode for DVB-ASI

• Jumper selectable non-reclock mode for SMPTE 310M (19.4Mb/s) signals or

any other SDI signal within the 143Mb/s to 1.5Gb/s range

• Fully hot-swappable from front of frame with no BNC disconnect required

• Independent isolated output drivers to ensure no cross channel loading

effects (i.e. no need to terminate unused outputs)

• Tally output on Frame Status bus upon loss of input signal for quality

monitoring

• VistaLINK® -capable for remote monitoring via SNMP (using VistaLINK®

PRO) when installed in 500FR  frame with 500FC VistaLINK® Frame

controller

Specifications:

Serial Video Inputs:

Standards:	SMPTE 292M (1.5Gb/s), SMPTE 259M (143 to 360Mb/s), SMPTE 344M 		(540Mb/s), DVB-ASI

Connector: 	1 BNC per IEC 61169-8 Annex A

Equalization: 	Automatic to 350m @ 270Mb/s, 110m @ 1.5Gb/s with Belden 1694A (or 			equivalent)

Return Loss:	> 15dB up to 1.0Gb/s, > 10dB up to 	1.5Gb/s

Serial Video Outputs:

Number of Outputs:	8 (Optionally reclocked)

Connector: 	BNC per IEC 61169-8 Annex A

Signal Level:	800mV nominal

DC Offset:	0V ±0.5V

Rise and Fall Time:	200ps nominal

Overshoot: 	< 10% of amplitude

Return Loss:	> 10dB up to 1.5Gb/s

Wide Band Jitter:	< 0.2 UI

Electrical:

Voltage:	+12V DC

Power:		5W

EMI/RFI:	Complies with FCC Part 15

Class A and EU EMC directive

Physical:

Number of slots:	1

Ordering Information:

500DA-HD	HD/SD SDI Reclocking Distribution Amplifier (1x8)

500DA-HD-N	HD/SD-SDI Non-Reclocking Distribution Amplifier (1x8)

Accessories:

500FC	VistaLINK® Frame Controller

CP-2116E-H	Remote Control Panel

CP-2232E	Remote Control Panel

Enclosures

500FR		Compact High Density Distribution Frame

S501FR	Standalone enclosure